## Slide 1: The Design of an AC-dc power supply for welding machines
Senior Design Project
By Iragena Bangamwabo
Student -Electrical Engineering

## Slide 2: Outline
Introduction
Objective
Project Description
Design Requirements
Design Constraints
Design Approach
Tasks
Timeline
Implementation of Tasks

## Slide 3: Introduction
A welding power supply is a device that provides electric current to perform a fusion of materials(usually metals or thermoplastics) by melting them, which requires a high current and high voltage.
Notes: The focuses this project is to design a circuit that will serve as a power supply to in a welding machine.

## Slide 4: Objective
The objective of this project is to design a power supply that will take a wide range of AC input voltage and convert it into a steady DC output voltage and high current output.
Notes: The objective of this project is to develop a power supply that will take a wide range of AC input voltage and convert it into a steady DC output voltage.

## Slide 5: Design Requirements
AC input voltage range: 120V – 600V
Single/three phase
DC output voltage: 285V
Output current: 50A
A circuit protection mechanism

## Slide 6: Constraints
Budget – Estimated $1000 based on:
            Materials
            Supplies
            Equipment
Limited Resources
            High voltage power source
            Software for design and simulation purposes

## Slide 7: Design Approach

## Slide 8: Implementation Plan
Tasks
Task 1. Design the AC-DC Rectifier
Task 2. Design a DC-DC converter
Subtask 1. Buck-Boost Converter Analysis
Subtask 2. Transfer function
Task 3. Design a control unit for the power supply
  Subtask 1. Design the compensator
  Subtask 2. Design a Voltage control Oscillator
  Subtask 3. design a Gate drive
Task 4. Design Verification
Subtask 1. Testing of the whole system
Subtask 2. System refinement
Task 5. Build the circuit
Subtask 1. Design of the PCB
Subtask 2. Perform soldering
Task 6. Testing and Refinement
System Diagram

## Slide 9: Timeline

## Slide 10: Implementation of task 1
Design of an a C-DC rectifier

## Slide 11: Selected Component
Power Diode: The selected power diodes that meet the parameters for this circuit are VS-1N2128A, manufactured by Vishay Semiconductors

## Slide 12: Rectifier System Diagram
When the positive half cycle of the supply D1, D2 diodes conducts in a series while diodes D3 and D4 are reverse biased.
During the negative half cycle, D3 and D4 diodes conduct in a series and diodes D1 and D2 switch off as they are now reverse biased configuration
The low pass filter is used to filter the output waveform due to high ripple effect of the DC output from the rectifier
Notes: The series inductor presents high impedance at the ripple current frequency.

## Slide 13: Simulation Results
Input Vs output wave form after low pass filter

## Slide 14: Three Phase Incorporated

## Slide 15: Simulation Results

## Slide 16: Implementation of Task 2
Design of DC-DC converter

## Slide 17: System Requirements
The converter will operate in DC steady state under the following conditions:
  V-in = 120V_RMS
  V_o = 285V
  P_o = 14.4KW
  f_S = 200kHz

## Slide 18: Calculating components values
= 84.706A
D = 0.626
L = 26.621μH
= 5μs
= 50.526A
= 5.64Ω
C = 40μF

## Slide 19: Spice Simulation
The circuit model shown below with calculated components values will be used for a SPICE simulation of the Buck-boost power supply

## Slide 20: Spice Simulation Input Vs Output
At Vin =120, 180
At Vin =400, 520

## Slide 21: Implementation of task 3
Design of the control Unit

## Slide 22: Block Diagram

## Slide 23: Error Amplifier
The purpose of this error amplifier is to counteract gains and phases contained in the out put of the buck boost converter that could jeopardize the stability of the system

## Slide 24: Formulas Used
)

## Slide 25: Pulse Width Modulation
To enhance the tracking performance of the PWM voltage controlled buck boost converter, an op amp and a 555timer network is used as a voltage controlled oscillator (VCO)
The 55timer will generate a triangular waveform which is passed to the inverting input of the comparator
By passing the input voltage to the non-inverting comparator input, a PWM waveform is produced.

## Slide 26: Simulation Results
The saw tooth is the output of the voltage controlled oscillator
The comparator generated pulsating waveform

## Slide 27: Gate Drive
In order for this system to operate it needs a switch that can handle a significant power levels to be able to work correctly.
For high frequencies, MOSFETs require a gate drive circuit to do the on/off operation at the desired frequency

## Slide 28: Simulation Results
During the on-time of the switch a small DC current flows keeping the gate in an on and off state.

## Slide 29: Full Circuit

## Slide 30: Simulation Results

## Slide 31: More Simulations

## Slide 32: Implementation of task 4
The Design of a pcb

## Slide 33: Importing Schematics

## Slide 34: PCB1

## Slide 35: PCB 2

## Slide 36: PCB Design

## Slide 37: Photo view

## Slide 38: Online trace-width calculator

## Slide 39: Acknowledgment
References
A. N. (2011, June 06). Power, Electronic Systems, Applications and Resources on Electrical and Electronic Project-Thesis. Retrieved December 04, 2017
Introduction of Three phase Half/Full Converter. (2017, January O5). Retrieved December 04, 2017
Tai-Ming, T. T. (1988, November). FIRING CIRCUITS FOR THREE-PHASE POWER ELECTRONIC CIRCUITS. Retrieved October, 2017.
CHAIJARURNUDOMRUNG, K, & AREERAK, K. (2011, April). Modeling and Stability Analysis of AC-DC Power System with Controlled Rectifier and Constant Power Loads. Retrieved November 04, 2017, from
Dr. Alvernon Walker Engineering Department
(UMES)

## Slide 40: THE End
Questions/ Comments